## Slide 1: Stress concentrations in Tunnel
Younus Ahmed Khan

## Slide 2
Single tunnels : section notation
Tunnel shape, size, and orientation may be fixed by overall design and construction considerations.
There is no opportunity to reduce stress concentration.
The stress concentrations are combinations of vertical and horizontal loads
Important to:
Estimation of stress concentration factors in compression and tension (Kc, Kt)
Determinations of rock mass strengths (Co, To) and preexcavation principal stresses along the tunnel route.

## Slide 3
Single tunnels
Both stress and strength are essential to calculating tunnel wall safety factors (Fc, Ft).
Relatively high safety factors, say 4 in compression and 8 in tension, indicate a high degree of stability and little need for an engineered support system.
Low safety factors, near 1, indicate the opposite and that some permanent support will be required.

## Slide 4
Single tunnels
The shape in Figure is symmetric about a vertical axis, but there is no symmetry about any horizontal axis as there is for circular, elliptical, and rectangular sections.
For this reason, no simple analytical formulas are available for estimating stress concentration factors for an arched back tunnel.
Numerical methods serves the purpose instead

## Slide 5
Single tunnels –Arched back: H/W = 1
Figure b shows the stress distribution that results when the preexcavation stress field is uniaxial and vertical (Sy = 1,
Sx = 0);
Figure c shows the result when the preexcavation stress field is uniaxial and horizontal (Sy = 0, Sx = 1), and
Figure c shows the hydrostatic case (Sy = Sx = 1).
The horizontal bar under the note K = 1 indicates the length of line for a stress concentration of one

## Slide 6
Single tunnels
In all cases, the tunnel axis is assumed to be parallel to a principal stress direction.
These results are based on the assumption of elastic behavior and do not depend on the construction sequence

## Slide 7
Under vertical load (Sy = 1, Sx = 0); tension nearly equal in magnitude to the applied compression appears at the center of the floor or bottom and at the crown, while high compressive stresses appear at the bottom corners and along the shoulders at the top of the ribs (vertical wall sections).
Single tunnels: H/W = 1, Sy = 1, Sx = 0,

## Slide 8
Single tunnels
Under vertical load, peak tensions in the floor and crown and rib compression are largely unaffected by height to width ratio (H/W).
Corner compression decreases nonlinearly with height to width ratio (but increases linearly with the reciprocal width to
height ratio)

## Slide 9
Single tunnels
In theory, a mathematically sharp, 90◦ corner, would result in an
infinite compressive stress concentration at the corner points.
In numerical analysis, the result is simply a high but not infinite stress concentration.
A rounded corner done deliberately or left to nature would reduce an extraordinarily high stress concentration

## Slide 10
Single tunnels
Natural reduction in the stress concentration occurs through yielding of the rock mass in the vicinity of the corner point.
Yielding at a point elevates stress concentration at neighboring
points. Thus, peak stress is lowered, while the average stress is raised in the vicinity of a point stressed beyond the elastic limit.
As long as yielding is localized, the threat to tunnel stability is negligible
If the stress concentration at the shoulder or top of the rib is tolerable, then the corner stress is also likely to be tolerable.

## Slide 11
Under a uniaxial but horizontal compression (Sy = 0, Sx = 1); the floor and crown are under high compressive stress, while the rib is under tension equal in magnitude to the applied compression.
Under horizontal load, peak tension in the rib remains largely unaffected, while compressive stresses at the floor, corner, and crown increase almost linearly with height to width ratio
Single tunnels: H/W = 1, Sy = 0, Sx = 1,

## Slide 12
When the applied vertical and horizontal stresses are equal (Sy = 1, Sx = 1); (hydrostatic preexcavation stress state), the results show no tension and reduced compressive stress peaks relative to the uniaxial cases.
Compressive stress concentration trends with
height to width ratio in the hydrostatic case, are also linear in height to width ratio
Tension is absent in all hydrostatic cases
Single tunnels: H/W = 1, Sy = 1, Sx = 1,

## Slide 13
Example 1 An arched back tunnel is planned with a height to width ratio of two. Estimate stress concentration factors in the floor and crown when the preexcavation principal stress ratio M = 1/4 and (a) the vertical stress is S1, (b) the horizontal stress is S1.
Single tunnels: Example Problems

## Slide 14
Single tunnels: Example Problems 1 Solution

## Slide 15
Single tunnels: Example Problems 1 Solution

## Slide 16
Single tunnels: Example Problems 1 Solution
In case (a),
Kfoor = (1)[stress concentration at floor from Figure + (1/4)[stress concentration from Figure 4.3b]
Kf = (Sy)[(−0.012)(W/H) − 0.939] + (Sx)[(0.712)(W/H) + 0.969]
= (1)[−0.963] + (1/4)[2.393]
Kf = −0.37
y = –0.012x – 0.939

## Slide 17
Single tunnels: Example Problems 1 Solution
K(crown) = (1)[stress concentration due to vertical S1 from Figure] + (1/4)[stress concentration due to horizontal (S1/4) from Figure]
Kcr = (1)[(−0.012)(2) − 0.939] + (1/4)[(1.056)(2) + 2.337]
= (1)[−0.963] + (1/4)[4.449]
Kcr = 0.15

## Slide 18
Single tunnels: Example Problems 1 Solution
K(crown) = (1/4)[stress concentration due to vertical S1/4 from Figure] + (1)[stress concentration due to horizontal (S1) from Figure]
In case(b)
Kf = (1/4)[−0.963] + (1)[2.393] = 2.15
Kcr = (1/4)[−0.963] + (1)[4.449] = 4.21

## Slide 19
Single tunnels: Example Problems 1 Solution
The orientation effect is considerable. When the major compression is vertical a noticeable tension is induced in the floor, but only a small compression occurs in the crown. When the major compression is horizontal, the floor tension and crown experience substantial compressive stress concentrations.

## Slide 20
Single tunnels: Example Problems 2
Example 2 An arched back tunnel is planned with a height to width ratio of two. Estimate stress concentration factors in the ribs when the pre-excavation principal stress ratio M = 1/4
and (a) the vertical stress is S1, (b) the horizontal stress is S1. These are same conditions given in Example 1.