## Slide 1: Surface Subsidence due to mining

## Slide 2
Figure 1 Trough subsidence over a longwall extraction
Subsidence is the lowering of the ground surface following
underground extraction of an orebody.
Subsidence is produced, to a greater or a lesser degree, by almost all types of underground mining.
Surface displacement may result from the redistribution of stresses associated with excavation or from mining-related activities such as de-watering
Subsidence can be regarded as being of two types – continuous and discontinuous.
Continuous or trough subsidence involves the formation of a smooth surface subsidence profile that is free of step changes
Discontinuous subsidence is characterised by large surface displacements over limited surface areas and the formation of steps or discontinuities in the surface profile.

## Slide 3
Crown holes (Figure a) arise from the collapse of the roofs of generally abandoned, shallow open workings.
Pillar collapse in old, shallow workings may lead to similar surface expressions of discontinuous subsidence as does crown hole formation. Such collapses may occur as a result of a deterioration in pillar strength with time or the imposition of additional load on the pillar by surface construction. Large-scale pillar collapse in a working
mine can produce discontinuous subsidence over a larger area with more serious effects.
Chimney caving, piping or funnelling (Figure b) involves the progressive migration of an unsupported mining cavity through the overlying material to the surface. Chimney caves are sometimes known as sinkholes.

## Slide 4
If chimney formation is sudden rather than progressive, the phenomenon is sometimes known as plug subsidence (Figure c).

## Slide 5
Chimney caving mechanisms
Three distinct chimney caving mechanisms may be identified, each associated with different geological environments
The first mechanism occurs in weathered or weak rock, or in previously caved rock.
It is a progressive mechanism that starts with failure of the stope roof or hanging wall on inclined surfaces.
If a stable, self-supporting arch cannot be formed, the failure may progressively propagate towards the surface as shown in Figure 3.
As material falls from the roof or from the propagating cave, it will bulk and will tend to fill the stope void.
Unless the stope is initially large and open, or unless sufficient material is progressively drawn from it, the stope will eventually become filled with caved material which will provide support for the upper surface and so arrest the development of the cave.
Figure 3 Progressive vertical chimney cave development in homogeneous material

## Slide 6
The second mechanism is also progressive, but occurs as a result of the unravelling of a discontinuous rock mass. The rock material itself may be quite strong and may not fail except in flexure. The mechanism is controlled by the regular discontinuities in the rock mass
The third mechanism, that of plug subsidence, differs from the other two in that it is controlled by one or more major structural features which provide low shear strength surfaces on which the plug of undercut rock may slide under the influence of gravity. In this case, the mass of rock will undergo essentially rigid-body displacement without breaking up or dilating. Thus, a vertical displacement at the stope boundary will result in a vertical displacement of similar magnitude at the surface.

## Slide 7
Caving is an often observed phenomenon associated with underground mining and begins with collapse of the back, roof, or hanging wall.