## Slide 1: Rock Slope Stability
Younus Ahmed Khan
Dept. of Geology and Mining
University of Rajshahi

## Slide 2
Stability of slopes is an important engineering topic because of economic impact on mining and civil enterprises. Failures may be costly in the extreme and have tragic personal consequences.
Steep slopes are favorable to the economics of surface mines, while low slope angles favor stability.
In civil works such as highway cuts, slope failures

## Slide 3
Soil slopes; Rock slopes
Analysis methods between soil and rock slopes differ significantly.
Weathered rock slope(e.g. granitic rock) behaves like soil slope, high strength rock fails as a rigid body in translation mode while low strength soil often fails as rigid body in rotation.

## Slide 4
A primary objective of slope stability analysis is estimation of a factor of safety for the considered slope and slide mass.
An intuitive formulation of a safety factor appropriate to
translational sliding is the ratio of resisting to driving forces acting parallel to the direction of translation,
Thus, for translational slides factor of safety,
where R and D are the total resisting and driving forces

## Slide 6
The factor of safety:
The factor of safety defined here is a global factor of safety in contrast to a local factor of safety (FS) that is defined as the ratio of strength to stress at a point.
A local factor of safety less than one indicates the elastic limit may be exceeded, yielding, and failure ensue, at the
considered point.
A global safety factor less than one implies yielding and failure over an extended failure surface and is indicative of collapse.

## Slide 7
In the case of rotational sliding, as shown in Figure,

## Slide 8
What constitutes an adequate safety factor is often a matter of engineering judgment, but may also be required by construction codes.
In surface mining and cut rock slopes, safety factors are usually near one. Soil-like slopes such as waste rock dumps may require a safety factor of 1.5 or so.
In any case, if an estimated safety factor is too low for the problem at hand, then remedial measures are required. There are always two choices for improving a factor of safety (1) increase resistance or (2) decrease driving forces or moments.

## Slide 9
Translational rock slope failures
Two important types of translational rock slope failures are (1) planar block slides and (2) wedge slides
Planar block slides
Planar block slides are possible when “joints” dip into a surface excavation and the excavation is long relative to height. Joints properties testing leads to friction angle and cohesion for joints (φj, cj) and intact rock between joints (φr , cr ).
Persistence p is defined as the ratio of joint area Aj in a joint plane to total area A composed of joint area plus area of intact rock ridges Ar between joint segments (A = Aj + Ar ), that is, p = Aj/A.

## Slide 10
A simple weighted average for rock mass properties may be obtained from:
If the failure surface is entirely joint, then p = 1. In this case, slope failure is very much like a rock block sliding down an inclined plane.
A special case occurs when one assumes that intact rock and joint friction angles are equal and joint cohesion is negligible. This case leads to the well-known Terzaghi model of jointed rock mass strength where φ = φr = φj and c = (1−p)cr = (Ar/A)cr . The range of rock mass friction angles is relatively large; as a rough guide 25◦ < φ< 55◦.

## Slide 11
Planar block slide volumes and forces: (a) volumes, (b) weight, (c) seismic–dynamic force, (d) surcharge force

## Slide 12
Planar block slide volumes and forces: (e) bolt forces, and (f) water forces.

## Slide 13
Figures with various forces to be considered in analysis. Weight is always present, so there is always a driving force, but other forces may be absent. Driving forces include the downhill components of:
1 slide mass weight Ws;
2 seismic force Ss;
3 surcharge force Fs;
4 water force Ps
The total driving force is
D = Ws + Ss + Fs + Ps

## Slide 14
Resisting forces include uphill components of frictional resistance mobilized by normal loads, cohesive resistance, and direct resistance from reinforcement (bolting):
1 slide mass weight W’n;
2 seismic force S’n;
3 surcharge force F’n;
4 reinforcement normal force N’b;
5 reinforcement tangential force T’b;
6 cohesive force C’;
7 water forces Pn, P’
n.
Normal forces are summed algebraically to obtain the net normal force available to mobilize frictional resistance to sliding. This net normal force is, in fact, the effective normal force

## Slide 15
The positive shear direction is down slope and parallel to the potential failure surface. In the normal direction, equilibrium
Requires,
where N is the normal reaction of the rock mass below the failure surface to the slide mass above.

## Slide 16
Computation of the various forces that enter the safety factor calculation begins with the most important force which is weight of the slide mass W. Although this calculation is straightforward and is simply the product of specific weight γ times slide volume V, that is,
W = γ V,

## Slide 20
Water pressure calculation
for rock slopes

## Slide 21
where the first term in brackets is now the average pressure, while the second remains the
wetted area of the failure plane.